# Agilent 1120 Compact HPLC with Agilent EZChrom Software

The Agilent 1120 Compact LC is an affordable, high quality HPLC system for routine standard analyses, that maximizes uptime, minimizes maintenance and provides the highest return on your investment. It was developed to address the needs of small to medium-sized labs that are mainly concerned with routine analyses using standard HPLC methods. The Agilent 1120 Compact LC optimizes performance, while minimizing complexity. It gives you the proven quality and performance you expect from the industry leader, in your choice of five easy to own, integrated, “all-in-one” configurations.

This system includes:

- Gradient Quaternary Pump

- Manual Injector

- Variable Wavelength Detector (UV-Vis Detector)

- Installation kit

- Agilent EZChrom Elite software (with Dongle)

| Agilent 1120 Infinity LC System - Performance Specifications |
| --- |
| Safety features | Extensive diagnostics, error detection and display, leak detection, safe leak handling, leak output signal for shutdown of pumping system. Low voltages in major maintenance areas. |
| Control and data evaluation | Agilent EZChrom Compact, Agilent Lab Advisor, Agilent ChemStation, Agilent EZChrom Elite |
| Communications | Controller-area network (CAN), RS-232C, APG Remote: ready, start, stop and shut-down signals, LAN |
| GLP features | Early maintenance feedback (EMF), electronic records of maintenance and errors |

| Agilent 1120 Infinity LC System – Performance Specifications Pumps (isocratic and gradient) |
| --- |
| Hydraulic system | Dual plunger in series pump with proprietary servo-controlled variable stroke drive, floating plungers and passive inlet valve |
| Settable flow range | 0.001 – 10 mL/min, in 0.001 mL/ min increments |
| Flow range | 0.2 – 10.0 mL/min |
| Flow precision | <0.07% RSD, or < 0.02 min SD whatever is greater, based on retention time at constant room temperature |
| Flow accuracy | ± 1% or 10 μl/min whatever is greater |
| Pressure | Operating range 0 – 60 MPa (0 – 600 bar, 0 – 8700 psi) up to 5 mL/min Operating range 0 – 40 MPa (0 – 400 bar, 0 – 5880 psi) up to 5 mL/min Operating range 0 – 20 MPa (0 – 200 bar, 0 – 2950 psi) up to 10 mL/min (all versions) |
| Pressure pulsation | < 2 % amplitude (typically < 1 %), at 1 mL/min isopropanol, at all pressures > 1 MPa (10 bar) |
| Compressibility compensation | User-selectable, based on mobile phase compressibility |
| Recommended pH range | 1.0 – 12.5, solvents with pH < 2.3 should not contain acids which attack stainless steel |
| Gradient formation (gradient pump or optional; two solvents) | Low pressure dual mixing/gradient capability using proprietary high-speed proportioning valve Delay volume 800 – 1100 μl, dependent on back pressure |
| Composition range | 0 – 95 % or 5 – 100 %, user selectable |
| Composition precision | < 0.2 % RSD, at 0.2 and 1 mL/min |

| Agilent 1120 Infinity LC System - Performance Specifications Manual Injector |
| --- |
| Agilent 1120 Infinity LC System Performance Specifications Variable Wavelength Detector Detection type Double-beam photometer Light source Deuterium lamp Wavelength range 190 – 600 nm Short term noise ± 0.35 × 10-5 AU, at 230 nm Drift 3 × 10-4 AU/hr, at 254 nm Linearity > 2 AU (5%) upper limit Wavelength accuracy ± 1 nm; Self-calibration with deuterium lines, verification with holmium oxide filter Band width 6.5 nm typical Flow cells Standard: 14- μL volume, 10-mm cell path length and 40 bar (588 psi) pressure maximum High pressure: 14- μL volume, 10-mm cell path length and 400 bar (5880 psi) pressure maximum Semi-micro: 5- μL volume, 6-mm cell path length and 40 bar (588 psi) pressure maximum |  |